## Slide 1: Network sustainability, green metrics, data models, and instrumentation
Alexander Clemm ludwig@clemm.org & Marisol Palmero mpalmero@cisco.com
IETF 118, Prague, Czech Republic
November 2023

## Slide 2: Approaches to improve sustainability
Structuring Challenges and Opportunities – draft-irtf-nmrg-green-ps
Protocol
Network
Equipment
Architecture
Management
Plenty of opportunities to explore: pollution-aware traffic steering, energy-aware VNF placement, schemes to retire idling resources, ...
What is actionable for us? Which areas promise the greatest impact? What are the enablers?

## Slide 3: The relevance of data
“You cannot manage what you cannot measure” (Peter Drucker)
  Compare effectiveness of alternatives
  Quantify impact (cost/benefit analysis)
  Enable control loops
Foundational requirement hence: data that can be used to observe, assess, quantify “environmental impact”
This happens to also be actionable in IETF
  Everybody will need this
  Standardized data will facilitate solutions
  Hence a priority for E-Impact (we hope)
Network
Configure
Monitor &
Observe
Determine Actions

## Slide 4: Metrics vs Data Models vs Instrumentation
Metrics
  What are the metrics that matter: for control loops, to assess and compare effectiveness
Data Models
  How do we represent and organize metrics
  How to relate them to different entities
Instrumentation
  How do we implement software to provide actual data instances
  May involve internal instrumentation on a device, but also measurements & supporting protocols
Define
Represent
Implement

## Slide 5: Metrics
Physical
level
Traffic
level
“Singular”
“Collective”
Equipment/ Device
Packets,
Flows
Paths
Network as a whole
can be obtained on a per-entity basis
needs to be aggregated across multiple entities
Green Networking Metrics: https://datatracker.ietf.org/doc/html/draft-cx-green-metrics-02

## Slide 6: Metrics
Physical
level
Traffic
level
“Singular”
“Collective”
Equipment/ Device
Packets,
Flows
Paths
Network as a whole
can be obtained on a per-entity basis
needs to be aggregated across multiple entities
Green Networking Metrics: https://datatracker.ietf.org/doc/html/draft-cx-green-metrics-02
The natural starting point
The end outcome of interest
Advanced, more speculative
topics

## Slide 7: Metrics space
Equipment/ Device
Energy consumption, energy utilization efficiency
Examples
Power consumption absolute / normalized, per chassis/line card/port, etc
Consumption ratings (datasheet stuff)
But it is not just about equipment power but about greenhouse gas emissions
Account for sources (e.g. energy mix), deployment context (e.g. HVAC)
Conversion factors between “power” and “carbon”

## Slide 8: Conversion is a choice?
Energy<unit>
CO2eq
emission factor
location
power factor
energy source
lifetime
time of the day: min/hourly/season
$$
?
who has to pay?
GHG Protocol*:
Scope 3 vs Scope 2 & 1
Reference Green House Gas Protocol* https://ghgprotocol.org/
Not an inclusive list of possible factors: e.g. deployment context (e.g. HVAC / “building tax”), amortization of embedded carbon
Notes: the model should be open enough to alleviate the assumption...
avoiding assumptions, or reducing assumptions

## Slide 9: POWEFF Data Model

## Slide 10: Metrics under POWEFF-derived
Metric | Description
Energy consumption (kWh) | This represents the energy consumed by the device. Represented by the Power Draw
Power to traffic ratio (watts/Gbps) | Power measure on device (watts) / Traffic throughput (Kbps)
Extrapolated CO2 emissions (g CO2eq) | Use current energy consumption (kwh) and the device geo-location (e.g. -34.6037°, -58.3816°) to query carbon factor (ie from Electricy Maps) and calculate extrapolated CO2 emissions
PSU ratio (%) | Power supply efficiency (offered powered vs consumed power)

## Slide 11: Sustainability Insights Framework
Data Standardization
Where?
PROVIDER
PROVIDER
PROVIDER
NON-YANG SYS
NON-YANG SYS
NON-YANG SYS
AGGREGATOR
COLLECTOR
COLLECTOR
PROCESSOR
Visualization

## Slide 12: Sustainability Insights Framework
Circularity
materials, R’s, packaging, transport, etc...=> YANG or any other language defining semantic is required
PROVIDER
PROVIDER
PROVIDER
NON-YANG SYS
NON-YANG SYS
NON-YANG SYS
AGGREGATOR
COLLECTOR
COLLECTOR
PROCESSOR
Visualization

## Slide 13: Sustainability Insights Framework
Optimization
What to Optimize?
Reduce CO2eq emissions
Reduce e-Waste
Reduce embedded carbon
Accuracy of the measurements
Simulated vs Real metrics
Cross Domain (Ex: Traffic Path Optimization based on energy constraints)
PROVIDER
PROVIDER
PROVIDER
NON-YANG SYS
NON-YANG SYS
NON-YANG SYS
AGGREGATOR
COLLECTOR
COLLECTOR

## Slide 14: Metrics space (contd.)
Flows
Paths
Network- at-large
Relate carbon footprint to flows and service instances
Function of volume and duration
Additional considerations for packet replication, loss, etc.
Carbon flow statistics, enable carbon-based accounting
Examples: Energy consumption / carbon footprint over duration of flow
Assess carbon intensity of paths and route alternatives
Energy-/ Carbon-/ Pollution-Aware Networking
Examples: Path energy/carbon ratings (function of carbon ratings of hops)
Totality of the picture aggregated across network-at-large
Consider also HVAC, hidden / non-instrumented devices
Examples: Total energy consumption (MWh), Network energy efficiency (MWh/PB)

## Slide 15: Individual Metrics Controversies
Do traffic-level metrics even matter
  Non-linearity of energy consumption
  Idle power very close to power at max capacity
  Traffic volume is subject to many tradeoffs – e.g. efficient encoding may incur cost in compute
  Verdict is out, non-linearity may not change, more research is needed that is enabled by such metrics
Holistic metrics vs discount factors
  Energy consumption – CO2 equivalents – greenhouse gas equivalents
  Formulas and discount factors may introduce inaccuracies; how far do we go
  Need to clearly document & maintain separately assumptions and conversion factors vs base metrics
Relating sustainability cost to utility being derived as measures of efficiency
  E.g. power consumption relative to traffic volume
  Input needs to be put in relationship with utility that is being derived
    Volume of traffic (e.g. W/GB)is a flawed measure of utility, but better alternatives are lacking
  Any one metric can paint a distorted picture and can be gamed
  It’s the holistic picture that counts

## Slide 16: Selected Open Issues
Data and metrics, specifically beyond device-level
  Consistently applied and broadly supported
Energy consumed ≠ greenhouse gas emissions
  Which conversion factors are needed & how are they precisely defined
  Energy mix, deployment factors, embedded carbon tax, CO2/GG equivalents
Dealing with imprecision and uncertainty
  Specify ranges vs absolute values in some cases (e.g. power consumption of links)
Measuring of utility delivered for efficiency measures
  Can we do better than traffic volume
Virtualization – do we need virtual energy metrics
Compliance and certification
  Including incentive structure for accurate instrumentation
Instrumentation of legacy equipment
+ on a practical level in IETF/IRTF, landing spots are not always clear

## Slide 17: Backup

## Slide 18: Context
Reducing greenhouse gas emissions to address climate change is one of mankind’s “grand challenges”
This challenge also extends to network technology
  How to reduce environmental impact of networks?
  How to make them more sustainable & what can we do at IETF?
E-Impact Program sponsored by the IAB
  Following several earlier activities: E-Impact workshop, side meetings at IETF 115-117
  Several Internet Drafts have begun to appear, loosely coordinated here
  Landing spots for those drafts are not always clear e.g. https://datatracker.ietf.org/doc/html/draft-cx-green-metrics-02: opsawg? ippm? somewhere else?